## Slide 1
COSC-3070 Programming Autonomous Robot
Autonomous Path Following and Obstacle Avoidance With mBot Neo
Huynh Ngoc Tai (s3978680)
Tran Quang Minh (s3988776)
Chau Tung Nguyen (s3976069)
Lecturer: Ginel Dorleon
"I declare that in submitting all work for this assessment, I have read, understood and agree to the content and expectations of the assessment declaration".

## Slide 2: Problem Overview

## Slide 3: Problem Overview
Autonomous robots are revolutionizing industries like logistics and transportation.
They rely on AI, computer vision, and sensors to interpret paths, detect signs, and avoid obstacles.

## Slide 4: Problem Overview
For the final project of the course, we are given 2 things, which is :
- Cyber Pi is the microcontroller – the brain of the robot.
- mBot2 Neo is the complete robot – includes wheels, motors, sensors.
CODE

## Slide 5: Project Setup

## Slide 6: Problem Overview
The aim of the project is to simulate read-world autonomous robot using simple sensors and vision systems, which then the robot will need to successfully navigate a maze-like environment following and act accordingly to the signs it will sensor, or the obstacles along the way like an AI powered robot in the real world.

## Slide 7: Problem Goal
It follows traffic rules: stop on red, go on green, slow on yellow, and even handle combinations like yellow-to-green transitions. It must also avoid static obstacles automatically and reroute in T-junctions when needed.
For the demo, the robot must navigate a complex maze using only onboard logic, no remote control or intervention.

## Slide 8: Methodology Implementation

## Slide 9: Methodology
Obstacle detection with ultrasonic sensors
Our method integrates three modules—path tracking, visual detection, and obstacle avoidance—into a unified loop.
Line tracking using RGB sensor
Visual sign detection with RGB sensor

## Slide 10: System Initialization and Event Handling
Wait for user to prompt
Stop Mode
Start Running
Check For Anymore Input
Detect Colour Mode
Triangle Button
Square Button
JoyStick Button

## Slide 11: Obstacle detection with ultrasonic sensors
Check if there’s anything in front of the car
Continue Running
Stop Running
Wait for 10s to see if obstacle is cleared
Turn 180 degree and run
Yes
No
No
Yes

## Slide 12: Line tracking using RGB sensor
base_power: the forward speed baseline
offset: deviation from center line (negative = left, positive = right)
kp: proportional gain to control steering strength
Motor speed formulas:
right_power = base_power - kp × offset
left_power = -1 × (base_power + kp × offset)

## Slide 13: Visual sign detection with RGB sensor
Stop the car, will wait for 10 seconds then turn back
Slow the car
Will tell the car to run after being stopped by red light
Quad RGB sensor will check the colour of the sign under it to perform action accordingly

## Slide 14: Implementation

## Slide 15: In-Detailed Values for Implementation
Parameter | Value | Purpose
base_power | 30% PWM | Normal speed (~0.25 m/s)
base_power slow | 25% PWM | Caution zone speed (~0.20 m/s)
k_p | 0.3 | Proportional gain for smooth steering
Obstacle threshold | 15 cm | Safe stopping distance
Timeout duration | 10 seconds | Before rerouting
Turn angle | 190° | Prevents re-entering same blocked path

## Slide 16: Creative Addon
Color Detected | Action | LED Feedback | Sound
Red | Stop completely, wait for green | Red | 261 Hz tone
Green | Resume motion at 30% PWM | Green | 659 Hz tone
Yellow | Slow to 25% PWM for 5 seconds | Yellow | 294 Hz tone
White | Continue line tracking at base speed | White | No tone

## Slide 17: Testing

## Slide 18: Testing
As per the requirement from the assignment, we decided to create a maze which satisfy most of the objectives the robot need to be able to do:
Avoid obstacle
Perform sign actions
Navigate when it meets T turn
….

## Slide 19: Result, Evaluation and Conclusion

## Slide 20: Result, Evaluation and Conclusion
Successfully completed tasks with decent-performing models.
The robot responded correctly to all sign-based instructions
Obstacle avoidance worked reliably under varied layouts.
Minor challenges like lighting and alignment drift were resolved through recalibration and logic tuning.

## Slide 21: Challenges
While yellow slows the robot and green resumes it, the logic for maintaining speed for the first GREEN transition then speeding up at the second GREEN was not explicitly coded as we only have 5 seconds for the slowdown time.
If an obstacle partially blocks the path, the robot does not drift laterally to rejoin; it instead waits and turns
The robot does not yet evaluate both directions at a T intersection to select an available path, it will perform a single pivot if blocked

## Slide 22
COSC-3070 Programming Autonomous Robot
Autonomous Path Following and Obstacle Avoidance With mBot Neo
THANK YOU FOR LISTENING TO OUR PRESENTATION AND WISH YOU A NICE DAY
"I declare that in submitting all work for this assessment, I have read, understood and agree to the content and expectations of the assessment declaration".